## Slide 1: Intuitive Guide to Fourier Analysis and Spectral Estimation
How explore Fourier analysis with Matlab
Charan Langton
Victor Levin
www.complextoreal.com
Copyright C. Langton

## Slide 2: Material
We will cover
Fourier series for CT signals
Discrete Fourier series
CT Fourier transform
DT Fourier transform
DFT/FFT
Using DFT to do spectral estimation
Periodogram
Autopower
Matlab code at: http://complextoreal.com/fftguide/

## Slide 3: Some acronyms
FA – Fourier analysis
CT – Continuous time
DT – Discrete time
FT – Fourier transform
CE – Complex exponential
FSE – Fourier series equation
FSC – Fourier series coefficients
FT/FFT – Fourier transform

## Slide 4
In 1841, Baron Joseph Fourier, a natural scientist, noted while working on a problem relating to heat transfer, that solution to differential equations such as this one
Consisted of a set of harmonic sinusoids.
The whole field of spectral estimation is based on this observation.

## Slide 5
This is Fourier analysis: Taking an unknown periodic signal and representing it by a set of harmonic sinusoids that are related to each other by a concept called harmonics.
Fourier Synthesis: Taking a bunch of selected harmonics, changing their coefficients and phase to create a desired periodic wave.

## Slide 6
It is actually composed of these three sine waves.
Here is a random looking wave, which is periodic.
This signal in Time-domain.

## Slide 7
Time and Frequency Domain views of a signal
In time-domain, we write this wave as summation of three sine waves of frequencies 1, 2, and 3 Hz of different amplitudes.
Frequency domain view is called the spectrum of a signal.

## Slide 8
Fundamental Frequency: a fundamental concept.
It is the lowest frequency in the target signal.
So to do FA, you have to know the range of frequencies in a signal.
An arbitrary fundamental wave and its harmonics.
Start with an arbitrary wave of frequency, f0.
Its second harmonic of frequency 2 times f0. (c) A third harmonic of frequency 3 times f0.
The fundamental frequency and the harmonics (basis functions.)

## Slide 9
Amplitude and phase
A sine and a cosine of the same frequency makes a set of harmonics, both have same frequency but are orthogonal to each other. We use both sines and cosines to synthesize a wave.
Phase shift
Phase
Amplitude

## Slide 10: Creating a pretty good-looking square wave by adding a bunch of sinusoids.
Synthesizing waves by adding a bunch of harmonics
If we use only cosines, we get a wave that is “even.”
If we use only sines, we get a wave that is “odd.”

## Slide 11
Another example of Fourier synthesis, a saw-tooth wave

## Slide 12
Here is the Fourier series equation

## Slide 13
Fourier analysis consists of computing the coefficients of this equation.
They are easy to calculate. Refer to Chapter 1 of Reference book, IGFASA

## Slide 14
Simple example: what are the Fourier series coefficients of this signal.

## Slide 15
Coefficients become the spectrum

## Slide 16
Magnitude and Phase Spectrum

## Slide 17
Power spectrum
Square the magnitude to compute the one-sided power spectrum.

## Slide 18
Summary
Fourier series is way to represent an un-known continuous-time (CT) periodic signal into certain basis functions. It is an estimate.
These basis functions are harmonic sinusoids of a certain fundamental frequency.
The spectrum of this CT periodic signal is discrete, because the values occur only at integer multiples of the fundamental frequency.
To do the FA, we need to select a starting frequency, called the fundamental frequency, the lowest frequency present in the target signal.

## Slide 19: Complex representation of CT signals
What Euler said
This equation is called the Complex Exponential.
Positive CE
Negative CE

## Slide 20
A CE is a 3-D function, a helix. Its projections are sine and cosine.

## Slide 21
Plotting the sum and the difference of CEs gives us the cosine and the sine wave.

## Slide 22
Representing the Fourier series using the CEs
It take two CE to represent a sine and cosine, one with positive index and the other with negative.

## Slide 23
Rewriting FSE using CEs

## Slide 24
New form of FSE with CEs

## Slide 25
The complex form of the FSE.
The coefficients of the complex form of FS are complex.

## Slide 26
Example: Complex FSC of

## Slide 27
FSC of the complex form - summary
The complex form of the FSE is simpler to manipulate than the trigonometric form.
But because it takes a double-sided index to represent a CE, the spectrum of the complex form is two sided.
Does that means, we have magically given birth to negative frequencies now? NO!
There is no such thing as negative frequency!
It is the index that is negative. The x-axis of the spectrum is always k times the real quantity, the fundamental frequency.

## Slide 28
Sampling of analog signals to create discrete signals
Discrete vs. Digital

## Slide 29
Creating a discrete signal from a continuous signal by sampling
You must sample a signal at a rate that is at least two times the maximum frequency in the signal.
Or you will get aliasing.

## Slide 30
Aliasing – a consequence of improper sampling
The sampling period, Ts is the time period between samples. There is no relationship between the sampling period and the fundamental period, T0 of the signal. They are independent quantities.
Here are some samples. To which frequency do they belong?
https://www.quora.com/What-is-Aliasing-in-digital-communication/answer/Charan-Langton-1?__nsrc__=4&__snid3__=4388028371

## Slide 31
Concept of digital frequency for discrete signals
To - time period of a CT signal
N0 - number of samples for a DT signal

## Slide 32
Discrete form of FSE
Fourier Series for discrete periodic signals
Fourier Series for continuous periodic signals

## Slide 33
Discrete harmonics
Whereas harmonics for a CT signal are an integer times the fundamental, k fo.
For DT signals, the idea of harmonics is different and often confounding.
There are only N – unique harmonics of a DT signal that is periodic with N samples.
These are termed by Ko, but are same a No.
Because of this, the coefficients repeat every Ko harmonics.

## Slide 34
A DT signal has a double sided spectrum of repeating coefficients.
The discrete signal with period = 10 in (a),
(b) the fundamental spectrum, (c) the true repeating spectrum.

## Slide 35
A DT signal has a double sided spectrum of repeating coefficients.
The discrete signal with period = 10 in (a),
(b) the fundamental spectrum, (c) the true repeating spectrum.

## Slide 36
Fourier series
  Continuous, periodic signals – has a discrete single-sided spectrum
    Infinite harmonics
  Continuous , periodic complex version – has a discrete but two-sided spectrum
    Infinite harmonics
  Discrete periodic signals – has a discrete repeating spectrum
    Only Ko unique harmonics
So what to do if the signal is NOT periodic.
The Fourier Series vs. the Fourier Transform

## Slide 37
We need a period to compute the Fourier series coefficients.
The period of a non-periodic (aperiodic) signal can be conceptually extended in the limit to infinity.
Now we can apply the Fourier series equation to aperiodic signals by setting the period to infinity.
Period of a periodic signal

## Slide 38
CT aperiodic signals have continuous coefficients (spectrum).
As we increase the period in (b), i.e., allow more time between the pulses, the fundamental frequency gets smaller, which makes the spectral lines move closer together as in (c).
In the limiting case, where the period goes to the spectrum becomes continuous.
Hence, FT of a CT (FTCT) signals is continuous, unlike FSC which are discrete.

## Slide 39
Fourier transform (CTFT) is a modified version of Fourier series,
without a period and no concept of a fundamental frequency.
Fourier series
Fourier series/transform, non-periodic
Fourier series coefficients
Fourier transform

## Slide 40
Comparing FS and FT

## Slide 41
CTFT of a lone square pulse

## Slide 42
Some important CTFTs

## Slide 43
CTFT gives only relative amplitudes.
The CTFT of a periodic signal can be considered a sampled version of the FSC. Because FSC are discrete, so is the CTFT for a periodic signal.
Unlike the CTFT of an aperiodic signal which is continuous, the CTFT of a periodic signal is discrete with the frequency resolution equal to the signal frequency.
CTFT also applies to periodic signals.

## Slide 44
We do the same thing we did with CTFT, but now we extend the discrete period to infinity.
In DTFT, there is no period.
All we have is the length of the signal. What we have is the period of the signal.
We have no idea what the signal looks like outside this length.
What about aperiodic DT signals?

## Slide 45
CT vs. DT signals Fourier transform
Aperiodic, CT signals
Aperiodic, DT signals

## Slide 46
CTFT is continuous
Non-repeating
DTFT is also continuous but
Repeats
Comparing CTFT with DTFT

## Slide 47
DTFT of a triangular pulse

## Slide 48
DTFT of a periodic signal

## Slide 49
Compare the CTFT of the CT signal in (c) with the DTFT of the same signal in (d). The DTFT looks the same as the CTFT but repeats.
Comparing CTFT and DTFT for periodic signals.

## Slide 50
The input signal of case 4 fits closest to physical signals.
DTFT of such a signal is continuous, an undesirable quality
The discrete form of the spectrum of case 4 is preferable.
There is a way to combine these two cases. This is where the DFT comes in.
We take a signal, and call all its samples, its period.
Hence, the length of the signal samples is presumed to be its period.
Now, this aperiodic signal becomes a periodic signal of period N.
The DTFT as shown in case 4, for such a case is discrete.
Although it is still a DTFT, we call it a Discrete Fourier transform (DFT).
Hence, DFT takes an aperiodic input signal of case 3 but by assuming that it is actually a periodic signal, returns the discrete spectrum of case 4. This is a useful transformation!

## Slide 51
The DFT borrows elements from both the discrete Fourier series and the Fourier transform.
DFT can be done on any arbitrary finite-length, uniformly sampled signal.
There is no need to know the real period of the signal, only the sampling frequency.
The DFT is easy to carry out in software.
The spectrum produced by the DFT discrete, unlike DTFT.
DFT is DTFT on a finite length signal

## Slide 52
DFT is a sampled version of the DTFT

## Slide 53
Understanding DFT x-axis

## Slide 54
It takes whatever you give it as the period.

## Slide 55
DFT as a sampled version of DFT, sampled at N points.

## Slide 56
Zero-padding

## Slide 57
What DFT does

## Slide 58
Adding a bunch of zeros at the end of the signal improves the resolution.

## Slide 59
Increase N, the DFT size, with zero padding, for better spectrum

## Slide 60
FT of a square pulse

## Slide 61
DFT repeats with sampling frequency

## Slide 62
The DFT of samples of a sinusoid of f = 1 Hz and N = 7, i.e. Fs = 7.
The DFT of the for N = 7 in (b) results in an ideal response.
When N is 9, 11 and 12, the result is noisy and not ideal as in (c), (d) and (e).
The DFT is again ideal when N = 14 as in (f).
Leakage

## Slide 63
When the number of samples in the DFT are not an integer multiple of the number of samples per cycle.
Or, when the end of the signal do not match and there is a discontinuity. It is a consequence of truncation.
Both of these are the same thing.
A perfect DFT requires that the size of the DFT (N) be exactly equal to integer maultiple of the sampling frequency.
This is called Leakage.
The spectrum appears to be leaking into adjacent bins.
Leakage

## Slide 64
Leakage seen another way as discontinuity, Fs = 7, f = 1

## Slide 65
Truncation

## Slide 66
Do longer DFT
Use a Window
What can we do about leakage

## Slide 68
FFT is a special fast algorithm for computing the DFT, with N a power of 2. 4, 8, 256, 1024, etc.
The DFT although easy to compute, requires a good number of calculations. For each harmonic, we have N multiplications and we do this N times, giving us approximately N^2 calculations, referred to as multiply-and-accumulate (MAC) operations in DSP. A 256-point DFT would require $65,792 calculations.
In 1965, Cooley and Tukey came up with a computational breakthrough called the Fast Fourier transform algorithm.
This was an ingenious manipulation of the inherent symmetry in the calculations. It is now used so commonly that DFT is very often known by the name FFT.
Fast Fourier Transform (FFT)

## Slide 69
FT does not exist for all signals.
Random signals are a class of signals, for which the FS and FT are not always valid.
Conditions for the existence of a FT

## Slide 70
We find that although the direct FT of a random signal may not exist, the FT of its auto-correlation function always exists.
So we have two ways of computing a power spectrum.
  The square of the DFT – Periodogram
  The DFT of the ACF - Autopower
Autopower and Periodogram

## Slide 71
The biased form of the ACF

## Slide 73
Autopower(Corellogram)

## Slide 74
Parameters of Autopower

## Slide 75
Lag size effect

## Slide 76
Periodogram

## Slide 77
Windowing the Autopower

## Slide 78
Signal size effect on Periodogram

## Slide 79
Window effect in Periodogram

## Slide 80
Improving Periodogram by averaging realization

## Slide 81
Averaging a number of periodogram was first proposed by Bartlett. The algorithm cuts the signal into smaller sub-segments which results in a less noisy spectrum, i.e., with a smaller variance.
Split the N points into K segments of length M points each. For each segment, compute the periodogram by computing the DFT, then square the magnitude and divide by M. Average the result of all K segments to get the averaged periodogram.
Bartlett and Welch methods to improve Periodogram

## Slide 82
The Welch method is modification of the Bartlett method by using overlapping segments. The data segment is split into L data segments of length M, overlapping by D points. The overlap, D can be 0% to 50%.
Apply window to each segment, do the periodogram of each segment and average the results.
Many different versions of this idea are discussed in [Poularikas book, 2009].
Welch method

## Slide 83
Comparing Autopower and Periodogram
Ref: Hayes book

## Slide 84
Use Autopower first
Use Periodogram, if Autopower not available
  Must average several DFTs.
  Results are usually acceptable.
What to use

## Slide 85: Thank you.
Charan Langton
charldsp@gmail.com
Copyright Charan Langton
Please credit if using figures from this presentation.

## Slide 86: References
[Langton2017] Intuitive Guide to Fourier Analysis and Spectral Estimation, Mountcastle Company 2017
[Brigham1988] Brigham, Oran E., Fast Fourier Transform, FFT and its Applications'', Prentice Hall, 1988.
[Gleason1995] Gleason, Alan., `Who is Fourier, A Mathematical Adventure'' Translational College of Lex, Language Research Foundation, Boston, 1995.
[Hayes1996] Hayes Monson H.Statistical Digital Signal Processing and Modeling, (1996), John Wiley \& Sons.
[Kay1988] Kay, Steven M., Modern Spectral Estimation, Theory and Applications, Prentice Hall, 1988.
[Lathi1998] Lathi, B. P., Modern Digital and Analog Communications. 3rd Edition, Oxford University Press, 1998.
[Lyons2013] Lyons, Rick., “Understanding Digital Signal Process'', Prentice Hall, 2013.
[Mandal2007] Mandal, Mrinal. and Asif, Amir., “Continuous and Discrete Time Signals and System'' Cambridge University press, 2007.
[Marks2009] Marks II, Robert J. , “Handbook of Fourier Analysis and its Applications'', Oxford University Press, 2009.
[Miller2004] Scott L. Miller, Donald G. Childers. Probability and Random Processes, Elesevier Inc., 2004.
[Mitra2006] Mitra, Sanit K., “Digital Signal Processing'', McGraw Hill, 2006.
[Oppenheim1997] Oppenheim, Alan V. and Willsky, Alan S. with S. Hamid Nawab., `Signals and Systems'', Second edition, Prentice Hall, 1997.

## Slide 87: References – con’td
[Percival1993] Percival, Donald B and Walden, Andrew T, Spectral Analysis for physical Applications, Multi-taper and conventional Univariate Techniques, Cambridge University Press, 1993.
[Poularikas2009] Poularikas, Alexander D., “Discrete Random Signal processing and Filtering Primer with Matlab'', CRC press, 2009.
[Priestley1981] Priestley, M.B., “Spectral Analysis and Time Series'', Academic Press, 1981.
[Rorabaugh2011] Rorabaugh, C. Britton, `Notes on Digital Signal Processing'', Prentice Hall, 2011.
[Smith2007] Smith, III, Julius O. , “Mathematics of the Discrete Fourier Transform (DFT): with Audio Applications'', W3K Publishing, 2007.
[Schwartz1977] Schwartz, Mischa and Shaw, Leonard., “Signal Processing: Discrete Spectral Analysis, Detection and Estimation'', McGraw Hill, 1977.
[Stein2000] Stein, Jonathon (Y).,”Digital Signal processing, a Computer Science Perspective'', Wiley Interscience, 2000.
[Stoica1997] Stoica, Petre, Moses, Randolph, Introduction to Spectral Analysis, Prentice Hall, 1997.
[Tervo2014] Tervo, Richard J., “Practical Signal Theory with Matlab Applications'', Wiley Interscience, 2014.
[Therrie2012] Therrie, Charles W. and Tummala, Murali, Probability and Random Process for Electrical and Computer Engineers. CRC Press, 2012.